## Slide 1
Electroencephalogram (EEG) Signal based Quantification of Stress Using Hybrid Deep Neural Network
Presented By:
Shahriar Nafis Dihan
Dept. of EEE
Roll:1901042
Mejbah Md. Fahim
Dept. of EEE
Roll: 1901056
Heaven’s Light is Our Guide
Department of Electrical & Electronic Engineering
Rajshahi University of Engineering & Technology
Supervised By:
Dr. Mohammod Abdul Motin
Associate Professor
Dept. of EEE
RUET

## Slide 2
Outline
1.Thesis Background
2.Literature Survey
3.Objectives
4.Methodology
5.Expected Outcome
6.Future Plan
02

## Slide 3
Introduction
Electroencephalography (EEG) signal is used to record electrical activity of the brain. This technique involves placing electrodes on the scalp to measure voltage fluctuations resulting from ionic current flows within the neurons of the brain. The recorded signals known as EEG signals.
What Is EEG Signal ?
Fig 1 : EEG Cap [1]
Fig 2 : EEG Signal [2]
03

## Slide 4
Stress & It’s Impact !
Introduction (Contd.)
It’s a psychological term about worry or mental tension caused by difficult situation.
Stress begins in the body through a complex interaction of the nervous system and Physical system.
Fig 3 : Impact of stress on daily life [3]
Fig 4 : Stress Curve [4]
04

## Slide 5
Literature Survey
Paper Name | Accuracy | Accuracy | Research Gap
StressNet: Hybrid model of LSTM and CNN for stress detection from electroencephalogram signal (EEG) [5] | LSTM+CNN | 97.8% | Evaluation limited to SEED and DEAP datasets, lacking broader applicability
Evolutionary inspired approach for mental stress detection using EEG signal [6] | SVM | 97.2559% | Overemphasis on SVM and feature extraction without exploring alternative or hybrid machine learning approaches.
L. D. Sharma, V. K. Bohat, M. Habib, A.-Z. Ala’M,H. Faris, and I. Aljarah, “Evolutionary inspired ap-proach for mental stress detection using eeg signal,”Expert systems with applications, vol. 197, p. 116634,2022.
S. A. M. Mane and A. Shinde, “Stressnet: Hybrid modelof lstm and cnn for stress detection from electroen-cephalogram signal (eeg),” Results in Control and Op-timization, vol. 11, p. 100231, 2023.
[5]
[6]
05

## Slide 6
Literature Survey(Contd.)
Paper Name | Model/Classifier | Accuracy | Research Gap
EEG Based Aptitude Detection System for Stress Regulation in Health Care Workers [7] | LSTM | 94% | The system is tailored for workplace environments and may not generalize well to other stress-inducing scenarios.
Detection of Negative Stress through Spectral Features of Electroencephalographic Recordings and a Convolutional Neural Network [8] | AlexNet | 84% | The model uses large windowing technique.
T. Khan, H. Javed, M. Amin, O. Usman, S. Ishtiaq Hus-sain, A. Mehmoood, and C. Maple, “Eeg based ap-titude detection system for stress regulation in healthcare workers,” Scientific Programming, vol. 2021, no. 1,p. 4620487, 2021.
A. Mart´ınez-Rodrigo, B. Garc´ıa-Mart´ınez, ´A. Huerta,and R. Alcaraz, “Detection of negative stress throughspectral features of electroencephalographic recordingsand a convolutional neural network,” Sensors, vol. 21,no. 9, p. 3050, 2021.
[7]
[8]
06

## Slide 7
Literature Survey(Contd.)
Paper Name | Model/Classifier | Accuracy | Research Gap
Modeling Mental Stress Using a Deep Learning Framework [9] | CNN | 82 % | It is a shallow model . It shows that this model needs to be further tuned and increase it’s complexity.
K. Masood and M. A. Alghamdi, "Modeling Mental Stress Using a Deep Learning Framework," in IEEE Access, vol. 7, pp. 68446-68454, 2019, doi: 10.1109/ACCESS.2019.2917718. keywords: {Stress;Biomedical monitoring;Heart rate variability;Feature extraction;Monitoring;Mental stress;cognitive experiments;deep learning;convolution neural networks},
[9]
07

## Slide 8
Objectives
  To design an efficient deep learning model to predict the stress .
08

## Slide 9
Dataset Description
Methodology
Simultaneous Task EEG workload (STEW) Dataset
Fig 5 : Simkap Test [10]
Subject | Signal Type | Signal Duration | Signal Sampling Frequency | No of Electrode
45 | EEG | 150 sec | 128 Hz | 14
Subjects were asked to perform the simultaneous Capacity (Simkap) test module of the Vienna Test System [10]
2 Classes | 3 Classes
Low : 1-5 High : 6-9 | Low : 1-3 Moderate : 4-6 High : 7-9
Output Label
Wei Lun Lim, Olga Sourina, Lipo Wang, July 10, 2018, "STEW: Simultaneous Task EEG Workload Dataset", IEEE Dataport, doi: https://dx.doi.org/10.21227/44r8-ya50.
[10]
Name | Value
Lower cut | 0.05 Hz
Higher cut | 45 Hz
Segment Size | 512
Overlap | 128
Order | 2
Butterworth Bandpass Filter
09

## Slide 10
Confusion Matrix
Fig 6: Confusion Matrix
Methodology (Contd.)
Precision =
Recall =
F1 score =
Accuracy =
10

## Slide 11
CNN Model Architecture :
Fig 7 : CNN Model Architecture
Methodology (Contd.)
Optimizer : Adam
Loss : Sparse categorical cross-entropy
Activation Function : SoftMax, ReLU
Train : 80 %
Test : 20 %
11

## Slide 12
Confusion Matrix
Classification report
Overall Accuracy : 77 %
Fig 8: Confusion Matrix
Methodology (Contd.)
12

## Slide 13
Methodology (Resnet_50)
7X7,64 stride 2
1X1 conv 64
3X3 conv 64
1X1 conv,256
1X1 conv, 128
3X3 conv, 128
1X1 conv, 512
1X1 conv, 256
3X3 conv,256
1X1 conv, 1024
1X1 conv, 512
3X3 conv, 512
1X1 conv,2048
Average pool
3X3 Maxpooling,stride 2
Dense layer 512
BatchNorm
Dropout 0.5
Dense layer 3
Low
Moderate
High
Raw Input
Data Preprocessing
Optimizer : Adam
Loss : Sparse categorical cross-entropy (3 classes)
Binary cross-entropy (2 classes)
Activation Function : SoftMax, ReLU
Train : 80 %
Test : 20 %
13

## Slide 14
Methodology (ResNet50)
Class | Precision | Recall | F1 Score
High | 0.98 | 0.95 | 0.96
Low | 0.94 | 0.98 | 0.96
Overall Accuracy : 96.92 %
14

## Slide 15
Methodology (ResNet50)
Class | Precision | Recall | F1 Score
High | 0.97 | 0.94 | 0.96
Low | 0.99 | 0.95 | 0.98
Moderate | 0.93 | 0.97 | 0.96
Overall Accuracy : 96.40 %
15

## Slide 16
Methodology (VGG16)
Optimizer : Adam
Loss : sparse categorical cross-entropy (3 classes)
Binary cross-entropy (2 classes)
Activation Function : SoftMax, ReLU
Train : 80 %
Test : 20 %
Fig 9 : VGG Model Architecture
EEG RAW INPUT
CONV 1D(64)
MAXPOOL1D
CONV 1D(128)
MAXPOOL1D
CONV 1D(256)
CONV 1D(64)
CONV 1D(128)
CONV 1D(256)
MAXPOOL1D
CONV 1D(512)
MAXPOOL1D
MAXPOOL1D
FLATTEN
DROPOUT(0.5)
DENSE(128)
DROPOUT(0.5)
DENSE(64)
DROPOUT(0.5)
DENSE(32)
OUTPUT DENSE(3)
CONV 1D(256)
CONV 1D(512)
CONV 1D(512)
CONV 1D(512)
CONV 1D(512)
CONV 1D(512)
Low
Moderate
High
16

## Slide 17
Methodology (VGG16)
Class | Precision | Recall | F1 Score
High | 1.00 | 1.00 | 0.99
Low | 1.00 | 1.00 | 0.99
Overall Accuracy : 99.77%
17

## Slide 18
Methodology (VGG16)
Class | Precision | Recall | F1 Score
High | 0.99 | 0.99 | 0.99
Low | 1.00 | 0.99 | 1.00
Moderate | 0.99 | 1.00 | 0.99
Overall Accuracy : 99.47 %
18

## Slide 19
Methodology (AlexNet)
High Moderate Low
EEG RAW INPUT
CONV 1D(96)
MAXPOOL1D
2nd CONV 1D(256)
MAXPOOL1D
CONV 1D(384)
MAXPOOL1D
4th CONV 1D(128)
MAXPOOL1D
FLATTEN
DROPOUT(0.5)
DENSE(4096)
DROPOUT(0.5)
DENSE(4096)
OUTPUT DENSE(3)
CONV 1D(384)
CONV 1D(256)
AlexNet Model Architecture :
Optimizer : Adam
Loss : Sparse categorical cross-entropy (3 classes)
Binary cross-entropy (2 classes)
Activation Function : SoftMax, ReLU
Train : 80 %
Test : 20 %
Fig 10 : AlexNet Model Architecture
19

## Slide 20
Methodology (Alexnet)
AlexNet binary classification
Finally the confusion matrix is being showed.
Results Overview
Display key performance metrics:
  Accuracy: 99%
  Macro Average F1 Score: 99%
  Weighted Average F1 Score: 99%
Confusion matrix
Class | Precision | Recall | F1 Score
High | 0.99 | 0.99 | 0.99
Low | 0.98 | 0.98 | 0.98
Overall Accuracy : 99.21%
20

## Slide 21
Methodology (AlexNet)
Finally the confusion matrix is being showed.
Results Overview
Display key performance metrics:
  Accuracy: 98%
  Macro Average F1 Score: 98%
  Weighted Average F1 Score: 98%
Confusion Matrix
Class | Precision | Recall | F1 Score
High | 0.97 | 0.98 | 0.97
Low | 0.98 | 0.98 | 0.98
Moderate | 0.99 | 0.99 | 0.99
Overall Accuracy : 98.36%
AlexNet three-class classification
21

## Slide 22
Methodology (temporal)
CNN + BLSTM ARCHITECTURE :
1DCNN
Raw EEG
Filtered EEG
Bandpass filter
0.5-45 Hz
1DCNN
BLSTM
Dense
layer
Output Layer
1DCNN
1DCNN
1DCNN
Fig 11 : Model Architecture
32 filters, kernel size=16,relu
16 filters, kernel size=8,relu
16 filters, kernel size=8 ,relu
16 filters, kernel size=8 ,relu
16 filters, kernel size=8 ,relu
64 neurons , tanh
BLSTM
64 neurons , tanh
40 neurons , relu
1 or 3 neurons , sigmoid/softmax
Optimizer : Adam
Loss : Sparse categorical cross-entropy
Binary cross-entropy
Activation Function : SoftMax, ReLU, Tanh
Train : 80 %
Test : 20 %
22

## Slide 23
Methodology (Temporal)
CNN+BLSTM :
Finally the confusion matrix is being showed.
Results Overview
Display key performance metrics:
  Accuracy: 91%
  Macro Average F1 Score: 90%
  Weighted Average F1 Score: 91%
Confusion matrix
Class | Precision | Recall | F1 Score
High | 0.93 | 0.93 | 0.93
Low | 0.87 | 0.88 | 0.87
Overall Accuracy : 91 %
23

## Slide 24
Methodology (Temporal)
CNN + BLSTM
Finally the confusion matrix is being showed.
Results Overview
Display key performance metrics:
  Accuracy: 85%
  Macro Average F1 Score: 83%
  Weighted Average F1 Score: 85%
Confusion matrix
Class | Precision | Recall | F1 Score
High | 0.76 | 0.80 | 0.78
Low | 0.82 | 0.78 | 0.80
Moderate | 0.93 | 0.92 | 0.93
Overall Accuracy : 85 %
24

## Slide 25
Methodology (Temporal)
ACCURACY COMPARISON :
Label | CNN +BLSTM | AlexNet | VGGNET | ResNet_50
2 classes | Accuracy = 91 % | Accuracy = 99% | Accuracy = 99.97 % | Accuracy = 96.92 %
3 classes | Accuracy=85 % | Accuracy = 98% | Accuracy = 99.47 % | Accuracy = 96.40 %
25

## Slide 26
Expected Outcome and Future Plan :
Using some pretrained model ,accuracy is well satisfactory. But when using the temporal model accuracy is quite low.
So now trying to use some complex model to increase the accuracy and find out the
most convenient model.
26

## Slide 27
References
https://www.google.com/search?q=eeg+cap&sca_esv=a334b21506059727&udm=2&cs=1&hl=en&biw=1396&bih=663&sxsrf=ADLYWILsU3rHUm5YXuM8oUGupC6Gwt_1PA%3A1717325824424&ei=AFBcZonDGaXvseMP0t6JwAk&ved=0ahUKEwiJw-md4byGAxWld2wGHVJvApgQ4dUDCBA&uact=5&oq=eeg+cap&gs_lp=Egxnd3Mtd2l6LXNlcnAiB2VlZyBjYXAyBBAjGCcyBRAAGIAEMgUQABiABDIFEAAYgAQyBRAAGIAEMgUQABiABDIFEAAYgAQyBRAAGIAEMgUQABiABDIFEAAYgARIvipQgwdY-hZwAngAkAEAmAHLA6ABqBiqAQM0LTe4AQPIAQD4AQGYAgigAvwYqAIKwgIHECMYJxjqAsICChAAGIAEGEMYigXCAggQABiABBixA8ICBBAAGAOYAxeIBgGSBwUxLjQtN6AH5C4&sclient=gws-wiz-serp#vhid=dinzuIX05N7luM&vssid=mosaic
[1]
https://www.google.com/search?q=impact+of+stress&sca_esv=a334b21506059727&udm=2&cs=1&hl=en&biw=1396&bih=663&sxsrf=ADLYWIK2Yws1oKbcj4d2xz-fR_X4tqxIKQ%3A1717326933600&ei=VVRcZu-nJIuphbIP1L6E8Ao&oq=im&gs_lp=Egxnd3Mtd2l6LXNlcnAiAmltKgIIADIEECMYJzINEAAYgAQYsQMYQxiKBTIKEAAYgAQYQxiKBTIIEAAYgAQYsQMyCBAAGIAEGLEDMgUQABiABDIIEAAYgAQYsQMyBRAAGIAEMggQABiABBixAzIIEAAYgAQYsQNIgx9QpQdYqgtwAngAkAEAmAHHA6ABgweqAQM0LTK4AQHIAQD4AQGYAgSgAqwHqAIKwgIGEAAYCBgewgIHEAAYgAQYGMICBxAjGCcY6gLCAg4QABiABBixAxiDARiKBZgDDYgGAZIHBTIuNC0yoAfZDQ&sclient=gws-wiz-serp#imgrc=L-HAwVQ8pR4fAM&imgdii=FKuVcL_bYEhfSM
[3]
https://www.google.com/search?q=stress%20peak%20vs%20performance%20graph&hl=en&udm=2&tbs=rimg:CTreJgn2zrRrYeLgDW0astbQsgIAwAIA2AIA4AIA&cs=1&sa=X&ved=0CB0QuIIBahcKEwjgipWd5ryGAxUAAAAAHQAAAAAQBw&biw=1396&bih=663&dpr=1.38#vhid=6xXsZuf1T4OuBM&vssid=mosaic
[4]
https://www.google.com/search?sca_esv=b085d2a81de27599&sxsrf=ADLYWIICUEkQ2caswOzvgc0aLGfFwQFMjQ:1717272843136&q=eeg+signal&uds=ADvngMjOfaSrNC2thZQzcNTI5fuXbWnpC-Ob_d5usnxH7AVb6FeNXfolfyXFsLb5Mmiq4d9Grj4c_QHWs7W9qgQKOqL3N2F5KIrN3cRMxMCzQvdJSb5hzIqcGjRdRgA68ZfLvmVXIJ2rYtiH2KNLBVfME-g4zfflAKgw32WgzYXy7lzntilqPi_FOQS40-zlwOxgYHkfv3AeASixVIYn4y7TDVAL1Zfa77NU2GeKdxqQlZ5QtmAgnIochiLk9XGbp6dvonkOxCBIt4BxwFoqec8OJG1G6-RERghkpIjyPUOHTHb34820Mco&udm=2&prmd=ivsnmbz&sa=X&ved=2ahUKEwiRrbDum7uGAxWLRmwGHc6VCXEQtKgLegQIDRAB&biw=1396&bih=663&dpr=1.38#vhid=1wu1dvtQP1indM&vssid=mosaic
[2]
27

## Slide 28
References (Contd.)
L. D. Sharma, V. K. Bohat, M. Habib, A.-Z. Ala’M,H. Faris, and I. Aljarah, “Evolutionary inspired ap-proach for mental stress detection using eeg signal,”Expert systems
with applications,
vol. 197, p. 116634,2022.
S. A. M. Mane and A. Shinde, “Stressnet: Hybrid modelof lstm and cnn for stress detection from electroen-cephalogram signal (eeg),” Results in Control and Op-timization, vol. 11, p. 100231, 2023.
T. Khan, H. Javed, M. Amin, O. Usman, S. Ishtiaq Hus-sain, A. Mehmoood, and C. Maple, “Eeg based ap-titude detection system for stress regulation in healthcare workers,” Scientific Programming, vol. 2021, no. 1,p. 4620487, 2021.
[9]
[6]
[7]
[5]
Wei Lun Lim, Olga Sourina, Lipo Wang, July 10, 2018, "STEW: Simultaneous Task EEG Workload Dataset", IEEE Dataport, doi: https://dx.doi.org/10.21227/44r8-ya50.
[10]
A. Mart´ınez-Rodrigo, B. Garc´ıa-Mart´ınez, ´A. Huerta,and R. Alcaraz, “Detection of negative stress throughspectral features of electroencephalographic recordingsand a convolutional neural network,” Sensors, vol. 21,no. 9, p. 3050, 2021.
K. Masood and M. A. Alghamdi, "Modeling Mental Stress Using a Deep Learning Framework," in IEEE Access, vol. 7, pp. 68446-68454, 2019, doi: 10.1109/ACCESS.2019.2917718. keywords: {Stress;Biomedical monitoring;Heart rate variability;Feature extraction;Monitoring;Mental stress;cognitive experiments;deep learning;convolution neural networks}.
[8]
28

## Slide 29
Thank You
29